## Slide 1
Re-Imagining water
Reuse, renewal, resilience, and research
CHESC July 10, 2020
Eric Veium, CEM. CEP –Energy, Utilities, and Sustainability

## Slide 2: Take Away
A process that makes the difference:
Look outside the box
Bring in partners early
Challenge conventional assumptions
Run the numbers
Find all of the value
Tell a compelling story

## Slide 4: 2035 Master Plan:
GROWTH
Enrollment increase to 25,000 (headcount)
1.3M GSF new Academic & Support Space
7,000 beds new student housing
380 units workforce housing
NEEDS TO GROW
Additional ~400 AF/yr of water
400k GPD of wastewater treatment capacity

## Slide 5
Scenarios:
Business as usual - buy more water, treat more waste water (default solution)
Purchase SLO City recycled water (doesn’t solve waste water)
Purchase CMC recycled water (doesn’t solve waste water)
On-site recycled water (solves both water and waste water!)
Recycled water feasibility study

## Slide 6: Best Solution
On-Campus Recycled Water System
Meet the needs of the Campus’ 2035 Master Plan
Renew and Expand Ag irrigation storage and distribution infrastructure across campus farm
Save the University $10M compared to next best alternative
Create a remarkable academic asset that will support Cal Poly‘s Learn-by-doing mission

## Slide 9: Reuse
Campus waste water collected to a single point
Waste water transported to Recycled Water Facility (WRF)
WRF produces 400AF/year of Title 22 Tertiary Treated Disinfected Recycled Water
Recycled water stored in surface reservoirs
Recycled water serves ag irrigation, landscape irrigation, new housing toilets, central plant cooling tower
WRF, Dairy Unit, Swine Unit solids, food waste, dairy process waste digested in lagoon digester and high rate digester
Digesters produce biogas used to power WRF fuel cell generator
Digesters produce nutrient-rich compost for field application on Cal Poly’s Farm reducing synthetic fertilizer and sequestering carbon
Recycled water source frees up potable surface water to support on-campus housing and Master Plan buildout.

## Slide 12: REnewal
College of Agriculture lacks resources to fund renewal of farm infrastructure
Donors want their name on a building not on an irrigation system
Project renews and enhances farm irrigation water distribution and storage infrastructure
Project renews and enhances Dairy waste management systems

## Slide 14: Resilience
Redundant waste water treatment infrastructure
Optimized use of shared infrastructure
Renewable/flex fuel backup power supply with high utilization

## Slide 16: Research
Campus as a Living Lab
Curriculum/Student Projects
  Agriculture, Natural Resources, Engineering, Science, many others
Research
  WRF Simulator/Optimization
  Water quality
  Soil health
  Carbon Sequestration
Wastewater Operator Training Program

## Slide 17: Take Away
A process that makes the difference:
Look outside the box
Bring in partners early
Challenge conventional assumptions
Run the numbers
Find all of the value
Tell a compelling story

## Slide 18
Additional Slides

## Slide 19
Two step design-build delivery
Build WRF plant in two 190 AF/yr phases – 2023 and 2028
Finance options:
  Campus or CSU Capital
  Equipment Lease Finance 2.5–3.0%, 12 year term
    For “repossessable assets only”
  Conventional loan 4.5–5.0%, 12 year term (or longer)
  WPA – Water Purchase Agreement (for package plant only)
    Own/operate vs. contract O&M vs. WPA considerations
    CAFES Fundraise?
Project delivery and finance options

## Slide 20
Campus or CSU Capital
Equipment Lease Finance 2.5–3.0%, 12 year term
  For “repossessable assets only”
Conventional loan 4.5–5.0%, 12 year term (or longer)
WPA – Water Purchase Agreement (for package plant only)
  Own/operate vs. contract O&M vs. WPA considerations
  CAFES Fundraise?
finance options

## Slide 21
Full buildout in one phase 2024 - $18.9M
Two phase own/operate:
  Phase I 2024 - $15M ($3.1M@3%, $11.9M@5% = $136K/mo, 144 mo’s)
  Phase II 2029 - $5M ($2.1M@3%, 2.9M Conv = $44K/mo, 144 mo’s)
  If in-house O&M, requires 2 FTE’s + Certification = $17.5K/mo + training costs
Two phase, WPA for package plant:
  Phase I 2024 - $13M ($1.8M@3%, $11.2@5% = $119K/mo, 144 mo’s)
  Phase II 2029 - $3M ($700K@3%, $2.3M@5% = $18K/mo, 144 mo’s)
  $17,000/mo O&M, no training costs, reduced regulatory risk
  *Costs for phase II delivery escalated by 5% CCI
Design and construction budget

## Slide 22
Two step design-build
Phase I – On line Jan 2024
  Lower sewer lift station near California entrance
  Force main (sewer line) to Dairy
  190 AF/yr package plant at Dairy
  100 AF Ag reservoir expansion for storage
  ~70% of CAFES irrigation piping
Phase II – On line Jan 2029
  Upper sewer lift station near Highland/Mt Bishop
  Second 190 AF/yr package plant at Dairy
  Remainder of CAFES irrigation piping
project delivery & construction phasing
Modular Package Plant

## Slide 23
Prior to issuance of RFQ/RFP:
  CEQA study - $350K
  Technical studies for design/permitting - $290K
  Total - $640K ($300K in hand from Utility surplus)
  One-time funding needed now to proceed - $340K
RFQ/RFP development
  Already funded and under contract w/Hartman
  Perform in parallel with CEQA
Ceqa, permitting and solicitation